PowerPoint Presentation
Transmission Media

---
Transmission medium and physical layer

---
Classes of transmission media

---
GUIDED MEDIA
Guided media, which are those that provide a conduit from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable.
Topics discussed in this section:
Twisted-Pair Cable
Coaxial Cable
Fiber-Optic Cable

---
Twisted-pair cable

---
UTP and STP cables

---
Table Categories of unshielded twisted-pair cables

---
UTP connector

---
UTP performance

---
Coaxial cable

---
Table 7.2 Categories of coaxial cables

---
BNC connectors

---
Coaxial cable performance

---
Fiber optics: Bending of light ray

---
Optical fiber

---
Propagation modes

---
Modes

---
Table Fiber types

---
Fiber construction

---
Fiber-optic cable connectors

---
Optical fiber performance

---
UNGUIDED MEDIA: WIRELESS
Unguided media transport electromagnetic waves without using a physical conductor. This type of communication is often referred to as wireless communication.
Topics discussed in this section:
Radio Waves
Microwaves
Infrared

---
Electromagnetic spectrum for wireless communication

---
Propagation methods

---
Bands

---
Wireless transmission waves

---
Radio waves are used for multicast communications, such as radio and television, and paging systems. They can penetrate through walls.
Highly regulated. Use omni directional antennas
Note

---
Omnidirectional antenna

---
Microwaves are used for unicast communication such as cellular telephones, satellite networks,
and wireless LANs.
Higher frequency ranges cannot penetrate walls.
Use directional antennas - point to point line of sight communications.
Note

---
Unidirectional antennas

---
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation.
Note

---
Wireless Channels
Wireless Channels
- Are subject to a lot more errors than guided media channels.
- Interference is one cause for errors, can be circumvented with high SNR.
- The higher the SNR the less capacity is available for transmission due to the broadcast nature of the channel.
- Channel also subject to fading and no coverage holes.